 WEEK -2 TASK

EFR32ZG28:

The EFR32ZG28 is a wireless SoC (System on Chip) developed by Silicon Labs as part of their EFR32 "Wireless Gecko" series. It is optimized for low-power and secure wireless communication, primarily used in Sub-GHz, Wi-SUN, and Proprietary RF applications.

Memory:
Flash : 512 KB
RAM : 64 KB

#### I/O and Peripherals
- GPIOs
- USART / I2C / SPI
- ADC / DAC
- Timers / PWM
- Crypto engine for AES-128/256, ECC, SHA-1, SHA-256
Core:
Family: ARM Cortex-M33 in EFR32ZG28
he EFR32ZG28 SoC (System on Chip) is built around the ARM Cortex-M33 core, which is highly efficient, secure, and low-power, making it perfect for IoT and wireless communication tasks.
Clock Speed : Up to 76.8 Mhz
Bit width : 32 bit
### TrustZone® Support
ARM TrustZone splits the system into two parts:
- Secure World – for sensitive tasks (e.g., secure boot, crypto, device keys)
- Non-Secure World – for general tasks (e.g., networking, sensors)
This enables secure OTA updates, crypto processing, and safe separation between app code and system-level security.
### DSP and FPU Support
- DSP (Digital Signal Processing): Allows efficient processing of signals, such as filtering, FFT, or analyzing sensor data in real-time.
  - Example: Processing environmental sensor data like gas levels, temperature, etc.
- FPU (Floating Point Unit): Hardware accelerator for floating-point math (e.g., float, double)
  - Example: Smooth BLE RSSI averaging, signal filtering, sensor fusion algorithms
CONTIKI -OS:
Contiki OS is a lightweight, open-source operating system designed for:
- IoT (Internet of Things) and wireless sensor networks
- Low-power embedded devices
- IPv6, 6LoWPAN, CoAP, RPL support (for networking in tiny devices)
- It runs directly on hardware (no other OS below it)
- Mostly written in C language.

Contiki-NG does not officially support EFR32ZG28
contiki-ng/
├── arch/ <-- Platform architecture
│ └── cpu/
│ └── arm/
│ └── cortex-m/ <-- Your core is here (Cortex-M33)
├── platform/ <-- Your EFR32ZG28 board files go here
│ └── efr32zg28/ <-- YOU create this
├── os/ <-- OS core
└── examples/ <-- For testing

CONTIKI OS INSTALLATION:
sudo apt update
sudo apt upgrade
sudo apt install git build-essential python3-pip srecord ccache
sudo apt install gcc-arm-none-eabi
 openocd screen
git clone https://github.com/contiki-ng/contiki-ng.git
 cd contiki-ng/
git submodule update --init –recursive

## Goal
Run a basic LED blink process on the EFR32ZG28 board using Contiki-NG, which does not natively support this platform.
contiki-ng/
├── arch/
│ └── platform/
│ └── efr32zg28/
│ ├── Makefile.include
│ ├── contiki-conf.h
│ ├── platform.h
│ └── dev/
│ ├── leds-arch.c
│ └── leds-arch.h
├── examples/
│ └── efr32zg28/
│ ├── blink.c
│ ├── Makefile
│ └── project-conf.h

### Create Platform Folder
mkdir -p ~/contiki-ng/arch/platform/efr32zg28

contiki-conf.h
device_config.h
 Makefile.efr32zg28
Makefile.include
 platform.c
platform.h
rtimer-arch.c
 rtimer-arch.h

Fix Makefile.include

### Board Configuration
BOARD = efr32zg28
BOARDS = efr32zg28

### Gecko SDK Path (verify this matches your installation)
GECKO_SDK = /home/abarnikag/SimplicityStudio/SDKs/gecko_sdk

### Device Configuration - MUST COME FIRST
CFLAGS := -DPART_NUMBER=EFR32ZG28A122F1024GM48 \
        -DDEVICE_FAMILY=efr32zg28 \
        -D__PROJECT__=\"EFR32ZG28\" \
        $(CFLAGS)

### Include Paths
CONTIKI_TARGET_DIRS += . ../../cpu/arm/cortex-m33
CFLAGS += -I$(CONTIKI)/arch/platform/$(TARGET) \
        -I$(CONTIKI)/arch/cpu/arm/cortex-m33 \
        -I$(GECKO_SDK)/platform/emlib/inc \
        -I$(GECKO_SDK)/platform/Device/SiliconLabs/EFR32ZG28/Include \
        -I$(GECKO_SDK)/hardware/kit/common/drivers \
        -I$(GECKO_SDK)/platform/CMSIS/Core/Include

### Source Files
CONTIKI_TARGET_SOURCEFILES += platform.c rtimer-arch.c

### Module Configuration
MODULES += $(CONTIKI_NG_ARCH_DIR)/platform/$(TARGET)

### Include ARM Cortex-M common makefile
include $(CONTIKI)/arch/cpu/arm/Makefile.arm

blink.c – Creating the Process
 Path: ~/contiki-ng/examples/efr32zg28/blink.c
## Makefile – Building the Example
Path: ~/contiki-ng/examples/efr32zg28/Makefile
Build the Blink file:
make TARGET=efr32zg28 clean
make TARGET=efr32zg28 BOARD=efr32zg28 V=1

Here I am Facing Error: