Date:25.06.25

OSI Model (Open System Interconnection):

OSI Model consists of 7 layers and each layer has specific functions and responsibilities.
Application Layer

Presentation Layer

Session Layer

Transport Layer
        → Segment
Network Layer
        → Data packet
Datalink Layer
        → Frame
Physical Layer
        Bit

Physical Layer:
      The lowest layer of the OSI reference model is the Physical Layer. It is responsible for the actual physical connection between the devices. Transmit the raw bits over the Medium .
      Ex: ethernet cable and USB,RS-232
Real world Protocol:
        Bluetooth,Wifi-signal ,USB
Data Link Layer
Responsible for MAC addressing, error detection
Data transfer between two devices on the same network
  (point to point protocol)
Real world protocols:
 Ethernet, WiFi, PPP, MAC, VLAN
Performs two local media-based functions:
- Access the media (Framing)
- Controls how data is placed and accessed from the media
     (Media Access Control)
     (Error Detection)
It refers only to physical links
Network Layer:
 Responsible for routing and logical addressing
 Assigns and handles IP addresses
Tools:
→ IP, ICMP, IPsec, OSPF, BGP
  (BGP → real gateway protocol)
Real world protocols:
→ IP (IPv4 / IPv6), ARP, RIP, OSPF,
  IPsec, ICMP
IP (IPv4 / IPv6): (Internet Protocol)
 It provides a logical addressing (IPv4, IPv6)
 and packet delivery secure to destination.
 Across networks. It is backbone of all internet communication.
ICMP: (Internet Control Message Protocol)
 Error reporting, network testing
 Help to detect unreachable ext (ping),
  host & network unreachable
OSPF: (Open Shortest Path First)
 Routing protocol to find shortest path in large networks.
IPSec: (Internet Protocol Security)
 It provides encryption, authentication,
  secure communication over IP.
Transport Layer:
 Data order & delivery
TCP – connection-oriented
Protocol used in web (HTTP), email
 Error control: Some data doesn't arrive at destination,
  automatic repeat request to retransmit the data.
UDP – connectionless
 No guarantee of delivery or order
 Used in: video, gaming, DNS
SCTP (Stream Control Transmission Protocol)
 End-to-end communication between two devices
- Segmentation:
   Breaks large data into smaller pieces
- Multiplexing:
   Uses port numbers to deliver data to the correct application
Session Layer:
This layer helps in session management, authentication
 Set up, manage the connection
  Apps:
    (Client ↔ Server diagram showing data packet transfer)
Protocols:
NetBIOS – Network Basic Input / Output System
 Allows applications on different
 computers to communicate over a LAN.
RPC – Remote Procedure Call
 Allows a program to call functions on
 another machine as if it were local.
### SIP: (Session Initiation Protocol)
 It is used to start, manage, and end voice/video calls over the Internet.
Use case: Online meeting, remote function call.
### Presentation Layer:
 Receives data from the application layer
 This layer shows how data is represented, formatted, and secured
 This function of Presentation layer call Translation
Handles translation, data compression, and encryption/decryption
The presentation layer will translate the machine-understandable binary format
Ex: ASCII → ABCD or 1234
SSL – Secure Sockets Layer
- Translation
- Data compression
- Encryption / Decryption
  Example binary:
DFGJY → 64E376 → 100110111 → 101010 → 1001101
### Application Layer:
It is the top-most layer
 Deals with network applications
Protocols:
- HTTP (Hypertext Transfer Protocol)
    Ex: Browsing websites
- FTP (File Transfer Protocol)
- SMTP (Simple Mail Transfer Protocol)
- MQTT (Message Queuing Telemetry Transport)
    → Lightweight protocol for IoT data transfer
      Used in: sensors, devices
- DNS (Domain Name System)
    → Resolves domain names to IP